## Slide 1
Pandora Hope, Chantal Donnelly, Louise Wilson, Justin Peter, Elisabeth Vogel, Wendy Sharples Bureau of Meteorology
Ensemble selection for hydrological projections – preliminary steps
Rainfall
Temperature
Wind
Radiation

## Slide 2: Hydrological Projections: the national picture
Commonwealth Scientific and Industrial Research Organisation (CSIRO) Sustainable Yields Projects

## Slide 3: National Hydrological Projections
Ensemble of climate forcing from GCMs
Multiple bias-correction + downscaling approaches
Continental in scale (# of Hydrological Models)
Complementary to existing hydrological projections landscape

## Slide 4: Confidence in projections: characterising uncertainty
Future GHG Concentrations
Changes in Global Climate
Changes in Regional Climate
Changes in Regional Hydrology
Regional climate modelling or statistical downscaling
Bias-Correction
Hydrological Modelling
Global Climate Modelling
Representative Concentration Pathways
3
5
5
1
=75 members
Notes: This diagram illustrates the modelling chain described in the previous slide, required to produce a set of hydrological projections
In order to properly sample the UNCERTAINTY in the climate systems response to changes in GHG concentrations, we must utilise an ensemble of GCMs.
And in order to use the output from GCMs – which have spatial scales in the order of 100 – 200km^2 per grid cell, we must downscale to the resolution of our hydrological model. In this case, 5km.
Depending on study location, or variable of interest, regional downscaling/ bias-corr or hyd modelling can be as uncertain as GCM – need to consider uncertainty in each component
The cascading set of lines below the schematic, represents the increase in the size of the overall ensemble, each time a new emissions scenario, or bias-correction and downscaling methodology is implemented
You can see that we quickly end up with a very large ensemble, which is good because it means we are characterising more of the uncertainty, which is an essential step for informing confidence in our projections

## Slide 5
Sample future emissions uncertainty

## Slide 6: Large to local scales
GCMs are the tool we use to gain insight into plausible future climates
GCMs output at spatial scales which are much larger than the scales of interest to users
Interactions at local scales are key, and so want to capture relationships between large and local scale features whilst retaining information about climate change from the GCM
Impact models are parametrised which means they are sensitive to bias from their host
Necessary to bias-correct GCM-inputs prior to downscaling
General Circulation Models
Regional Circulation Models
Impact Models
Bias-Correction & Scaling

## Slide 7
Sample response uncertainty: ensemble of GCMs

## Slide 8: Global Climate Model Selection
CMIP5 has data from over 40 models available.
For impact studies, rather than using the full suite of models, often 3 or 4 models are selected.
The aim is that these models encapsulate the 'range' of projections
This can be identified using tools on climatechangeinaustralia.gov.au
Warmer and little change: MIROC5
Hotter and drier: ACCESS1.0
Hotter and much drier: ACCESS1.3

## Slide 9: Global Climate Model (GCM) selection
Choose Models Based Upon:
the range of climate they simulate (hotter, less warm; wetter, drier).
their ability to capture important process (e.g. aerosols), have lower biases (e.g. ENSO), capture weather features of importance to Australia (e.g. blocking), and the seasonal cycle for a specific region.
Pragmatic choices:
which ones have been downscaled
which ones have the relevant data fields available
which ones have been used in other hydro projections?

## Slide 10: GCM selection based upon model's ability to simulate features of Australia's climate – including seasonal cycle
Projections for NRM (climatechangeinaustralia) defined a subset of 8 GCMs which was felt to adequately sample the full range of projections for the Australian region:
ACCESS1-0, CESM1-CAM5, CNRM-CM5, GFDL-ESM2M, HadGEM2-CC, CanESM2, MIROC5, NorESM1-M
Climate Change In Australia Technical Report, 2015
Notes: Seasonal cycle of rainfall

## Slide 11: Capture weather features well
For Instance
ACCESS1.0, ACCESS1.3 BCC_CSM1.1, NorESM1-M, CMCC-CM, CNRM-CM5 GFDL-ESM2G, GFDL-ESM2M, CNRM-CM5, GFDL-ESM2G, CMCC-CM
BCC_CSM1.1(m) (blocking poor), CMCC-CMS (storm tracks poor) HadGEM2-CC (blocking poor) INM-CM4.0 (jets poor), IPSL-CM5A-MR (storm tracks poor) MPI-ESM-LR (storm tracks poor) MRI-CGCM3 (blocking poor)
July
January
Grose et al. 2017

## Slide 12: Climate models that include a representation of the indirect aerosol effect and cloud lifetime and also capture the processes that influence southern Australian rainfall well, along with a reasonable representation of ENSO are: ACCESS1.0, ACCESS1.3, NorESM1-M, MRI-CGCM3
Brown et al. 2016
'Cold tongue' bias of ENSO

## Slide 13
Model Selection: ACCESS1.0, ACCESS1.3, MRI-CGCM3, NorESM1-M
CCIA: ACCESS1-0, CESM1-CAM5, CNRM-CM5, GFDL-ESM2M, HadGEM2-CC, CanESM2, MIROC5, NorESM1-M
Choice: ACCESS1.0, NorESM1-M

## Slide 14: Inter-Sectoral Impact Model Intercomparison Project (ISI-MIP)
IPSL-CM5A-LR GFDL-ESM2M MIROC5 HadGEM2-ES
RCP2.6, RCP6.0
NorESM1-M was good, but did not have near-surface winds available.
1861 to 2005
Frieler et al. 2017

## Slide 15
GFDL-ESM2M
ACCESS1.0
MPI-ESM-LR
DJF
MAM
JJA
SON

## Slide 16
Wind Speed
Uwnd
Vwnd
Precip
Which variables change the most?
Rainfall
Temperature
Wind
Radiation
ACCESS1.0

## Slide 17
Sample response uncertainty: ensemble of GCMs
Need to bias-correct and downscale GCM output before input into hydrological model.
Use a suite of approaches:
Empirical methods
Statistical methods
Dynamical models

## Slide 18
 | Description | Caveats | Examples
Change factor / scaling | Computationally inexpensive Conceptually simple Transfer function can be as simple as a delta change, or quantile based | Cannot add new information Cannot account for systematic changes or changes to feedback processes Assumes time invariant biases | Chiew method (MODSIM, 2017)

## Slide 19
 | Description | Caveats | Examples
Change factor / scaling | Computationally inexpensive Conceptually simple Transfer function can be as simple as a delta change, or quantile based | Cannot add new information Cannot account for systematic changes or changes to feedback processes Assumes time invariant biases | Chiew method (MODSIM, 2017)
Statistical | Based on relationship between large scale circulation and observations Relatively inexpensive (compared to dynamical downscaling) | Can add some new information by way of increased skill (relationships from large to local scale) Not internally consistent Assumes time invariant relationships | BoM-SDM (Timbal, 2009) NHMM (Potter, 2018) MRNBC (Johnson & Sharma) GLIMCLIM (Frost, 2011) ISIMIP2b (Frieler, 2017)

## Slide 20
 | Description | Caveats | Examples
Change factor / scaling | Computationally inexpensive Conceptually simple Transfer function can be as simple as a delta change, or quantile based | Cannot add new information Cannot account for systematic changes or changes to feedback processes Assumes time invariant biases | Chiew method (MODSIM, 2017)
Statistical | Based on relationship between large scale circulation and observations Relatively inexpensive (compared to dynamical downscaling) | Can add some new information by way of increased skill (relationships from large to local scale) Not internally consistent Assumes time invariant relationships | BoM-SDM (Timbal, 2009) NHMM (Potter, 2018) MRNBC (Johnson & Sharma) GLIMCLIM (Frost, 2011) ISIMIP2b (Frieler, 2017)
Dynamical | Resolves physical processes using GCM output as boundary conditions Better in areas with significant land surface processes | Computationally expensive Can add new information, especially in regions of complex topography and along coastlines | WRF (CMIP5 CORDEX runs) CCAM (CMIP5)

## Slide 21: Which GCMs have Downscaled Result Available??
Statistical:
BoM Statistical Downscale Method: 22 models.
ISI-MIP IPSL-CM5A-LR GFDL-ESM2M MIROC5 HadGEM2-ES
Dynamical:
CCAM: ACCESS1.0, CCSM4, CNRM-CM5, GFDL-CM3, MPI-ESM-LR, NorESM1-M
WRF, NARCliM new: ACCESS1.3; To come: ACCESS1.0, CanESM2,
COSMO: EC-EARTH, MPI-ESM-LR

## Slide 22: Comparison of downscaled results with observations
From CORDEX Giovanni Di Virgilio (in press, Giovanni@unsw.edu.au)

## Slide 23
Fig. 4 Summer (DJF) maximum temperature bias with respect to AGCD observations with stippling as per Fig. 3
Observed Tmax DJF
Downscaled anomaly

## Slide 24
Fig. 5 Winter (JJA) maximum temperature bias with respect to AGCD observations with stippling as per Fig. 3
Observed Tmax JJA
Downscaled anomaly

## Slide 25
Fig. 12 Annual mean precipitation bias of the RCMs with stippling as per Fig. 3
Observed Precip Annual
Downscaled anomaly

## Slide 26
Fig. 11 Probability density functions of mean daily precipitation across Australia

## Slide 27
Bias-corrected and downscaled inputs
AWRA-L
Sample response uncertainty: ensemble of GCMs

## Slide 29: Conclusion – which GCMs to do hydrological projections from?
We now have an understanding of the strengths and weaknesses of models, when we include them.

## Slide 30: National Hydrological Projections
Ensemble of climate forcing from GCMs
Multiple bias-correction + downscaling approaches
Continental in scale (# of Hydrological Models)
Complementary to existing hydrological projections landscape
Pandora Hope
Pandora.Hope@bom.gov.au
03 9669 4774
Louise Wilson, Chantal Donnelly
Thank you

## Slide 31
Thank you
Pandora Hope
Pandora.Hope@bom.gov.au
03 9669 4774